## Slide 1: Production Scheduling Optimization

## Slide 2: Problem Statement
What to produce?
When to produce?
How much to produce?
Factor | CO Time | Inventory Cost
Increase in frequency of changeover | Increase | Decrease
Decrease in frequency of changeover | Decrease | Increase
From-To product combination | Increase/decrease based on product combination | -
P1
P3
P2
P3
P4
P2

## Slide 3: Scopes & Assumptions
System Under Consideration: AL- CHEWY PROCESSING LINE
Total 9 SKUs (main flavors: ALMOND,PEANUTS, FRT NUT, CHOC PRETZEL NUT, REESES, GOLDEN GRAHAMS)
MILP Model is developed with objective to minimize total cost
Total Cost = CO Cost + Inventory Holding Cost + Penalty Cost + Overflow Cost
CO Cost = CO Time(day) * Line Rate (EA/day) * Product Cost * Profit Margin ($/unit $)
Inventory Holding Cost = 9% per year per unit $ of product * Excess Inventory * product cost
Penalty Cost = Profit Margin * Inventory Shortage
Overflow Cost = Profit Margin * Excess Inventory above Max DOS
Cost of single product = 1$
Excess Inventory = Current Inventory – Safety Stock
Inventory Shortage = Safety Stock – Current Inventory
Considering product will run at least a day if it starts running

## Slide 4: Follow Ups

## Slide 5: Parameters & Decision Variables
Set:
Parameters:
Decision Variables:
Auxiliary Variables:

## Slide 6: MILP Problem Formulation
Objective Function (Minimize Total Cost):
CO Cost
Inventory Cost
Constraints:
Logical relationship among decision variables
To make constraint (1) linear,
In a given time period only single product can be run on a Line
Relationship among production, demand, inventory, excess inventory and inventory shortage

## Slide 7: Cost Sensitivity Analysis
Assumptions:
Average Line Rate: 1.5 M EA/day
Average Profit Margin of products: 35%
Beginning Inventory = Safety Stock
Product Cost/EA = 1 $
Interest Rate= 9%
If we observe 1 hr of changeover in a year,
Amount of product loss = Line Rate * CO Time = 1.5 M*1/24 = 62,500 EA
CO Cost= Amount of production loss * Product Cost * Profit Margin = 62,500*35% = $ 23,000
Amount of inventory shortage = Line Rate * CO Time = 1.5 M*1/24 = 62,500 EA
Penalty Cost = Amount of inventory shortage * Product Cost * Profit Margin= 62,500 *35% = $ 23,000
Similarly, if we did not observer CO, we could produce product during the time and hold it for a year,
Excess Inventory above Safety Stock = Line Rate * CO Time = 1.5 M*1/24 = 62,500 EA
Holding Cost = Excess Inventory above Safety Stock * product cost * Interest Rate = 62,500*1*9% = $ 4,300
Penalty Cost and CO Cost are 5 times higher than Inventory Holding Cost